## Slide 1: Modelling of self-excited forces for long span bridges.
Ole Øiseth

## Slide 2: What is self-excited forces?
Aerodynamic forces du to the motion of the section
  Depends on displacements, velocities and accelerations

## Slide 3: Why are self-excited forces important?
Aerodynamic stiffness
Aerodynamic damping

## Slide 4: Why are self-excited forces important?
Ultimate limit state
  Stability issues (Flutter, static divergence)
  Wind induced load effects strongly depends on damping
Serviceability limit state
  Wind induced response strongly depends on damping

## Slide 5: Available models for self-excited forces
Quasi-steady models
  Neglects the fluid memory effect
  Can give inaccurate results
  Corrected quasi-steady theory can give excellent results, if used correctly
Unsteady models
  Easy to use in frequency domain
  Challenging in time domain? Depends on the quality of experimental data…
Nonlinear models
  Most are based on quasi-steady assumptions
  Can be challenging to obtain all parameters for the unsteady models

## Slide 6: The Wagner function
Analytical expression (Wagner 1925)
  Lift force after a step change in circulation (downwash)
  Potential flow, Kutta condition

## Slide 7: Theodorsen’s function
Analytical expression (Theodorsen 1934)
  Lift force for an oscillatory motion
  Potential flow, Kutta condition

## Slide 8: Wagner vs Theodorsen
Constitutes a Fourier Transform pair (Garrick 1938)
  Developed using the same assumptions, but for a different motion
Step response
Frequency response

## Slide 9: The convolution theorem
Convolution in one domain equals point wise multiplication in the other domain
FT input
FT IRF-> FRF
FT Output
Input
Impulse response function
Output

## Slide 10: Aerodynamic derivatives
Similar to Theodorsen’s function
Valid for a single harmonic motion with reduced frequency K

## Slide 11: Aerodynamic derivatives
Experimental results

## Slide 12: Aerodynamic derivatives
The model is linear
Transfer function defined by aerodynamic derivatives
FT motion
TF Motion->Force
FT Motion induced forces

## Slide 13: Rational functions
We need to fit curves to the experimental data
  Aerodynamic derivatives available at discrete reduced frequencies
Rational functions have often been used
  Other alternatives: indicial functions
Consider the real and the imaginary part

## Slide 14: Convolution integrals
Fit to experimental data
Convolution theorem

## Slide 15: State space model
Convolution integral →State space model
  Consider the frequency response
Frequency response → State space model
Use velocity as input instead of displacements

## Slide 16: State space model
Frequency response → state space model
  Jordan form (several other alternatives)
Input: Motion
Output: History dependent forces

## Slide 17: Implementation in FE software
Can be implemented as a user element
  We solve the state variables at the element level.

## Slide 18: Potential problems
Experimental data only available in a limited range
  In particular for free vibration tests
  Can give negative damping for modes not covered by experimental data
Is it necessary to identify aerodynamic derivatives?
  No! It is possible to identify the state space model directly

## Slide 19: System identification
Identify the input → output relation of a system
Optimize input to get the best possible identification
  Input: Unit step function, impulsive, harmonic, white noise, actual bridge motion…
Motion
Forces

## Slide 20: A new experimental setup
Designed to move the section in an arbitrary motion

## Slide 21: A new experimental setup
6 Axis load cells

## Slide 22: Aerodynamic derivatives
Standard test

## Slide 23: Aerodynamic derivatives
Standard test

## Slide 24: Dynamic system driven by white noise
The motion is similar to a buffeting free vibration test
White noise
Narrow
band motion
Self-excited forces

## Slide 25: Rectangular spectrum
White noise not possible → Rectangular spectrum
Self-excited forces
Motion

## Slide 26: Flutter vibration mode
Verify the load model along the structure
  The flutter mode is complex
    Time dependent
    The motion is different along the span (in particular for multimode flutter)

## Slide 27: Aerodynamic derivatives
Rectangular spectrum 0→3Hz
  One velocity V=10 m/s

## Slide 28: Aerodynamic derivatives
Aerodynamic derivatives related to velocities

## Slide 29: Aerodynamic derivatives
Aerodynamic derivatives related to displacements

## Slide 30: Concluding remarks
Unsteady models
  It is possible to include advanced unsteady models for self-excited forces in time domain
New experimental setup
  Easier to test the load models
Accuracy of the models
  We will look further into the accuracy of the current models
    The models might not work as well for some cross-sections